## Slide 1
CLINICAL PATHOLOGY RESIDENCY LECTURE SERIES
CLINICAL CHEMISTRY · LECTURE 1 OF 5
Analytic Techniques & Sources of Error
Methods, Interferences, and the Testing Cycle
Dr. Tamima El-Jisr
Chairperson, Department of Laboratory Medicine
Makassed General Hospital, Beirut
Clinical Pathology Residency Curriculum

## Slide 2
CLINICAL CHEMISTRY · FRAMING THE PROBLEM
Why This Matters
HIL
Hemolysis, icterus, lipemia — the everyday interferences that corrupt results
Hook
Very high analyte can read falsely LOW on a sandwich immunoassay
70%
Most laboratory errors are preanalytic — before the analyzer ever runs
A result is only as good as the method behind it. Knowing what each platform measures — and how it fails — lets you spot the impossible value, defend the real one, and advise clinicians who trust the number.
The consultative question is rarely 'what is the value?' — it is 'can I believe this value in this patient?'
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 2

## Slide 3
CLINICAL CHEMISTRY · LECTURE 1 OF 5
Learning Objectives
1
Describe spectrophotometry, immunoassays, and mass spectrometry at a working level.
2
Contrast sandwich and competitive immunoassay designs.
3
Recognize hemolysis, icterus, and lipemia interferences and their direction.
4
Identify the hook effect, heterophile-antibody, and biotin interferences.
5
Classify error across the preanalytic, analytic, and postanalytic phases.
6
Apply basic quality-control concepts to detect analytic error.
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 3

## Slide 4
CLINICAL CHEMISTRY · WHAT WE WILL COVER
Roadmap
1
Core methods — spectrophotometry, immunoassay, mass spectrometry
2
Immunoassay design & pitfalls — sandwich vs competitive; hook, heterophile, biotin
3
Sample interferences — hemolysis, icterus, lipemia
4
The testing cycle & QC — preanalytic to postanalytic error
5
Cases & board review — recognizing the impossible result
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 4

## Slide 5
01
PART ONE
Core Analytic Methods

## Slide 6
CLINICAL CHEMISTRY · METHODS
Spectrophotometry & Chromatography–MS
SPECTROPHOTOMETRY
Beer-Lambert law: absorbance is proportional to analyte concentration and path length.
The basis of most routine chemistry (enzymatic and colorimetric assays).
Endpoint vs kinetic (rate) measurements; enzyme activity is measured kinetically.
Turbidity from lipemia and color from hemolysis/icterus distort absorbance.
CHROMATOGRAPHY & MASS SPECTROMETRY
LC-MS/MS and GC-MS separate compounds then identify them by mass-to-charge.
High specificity — the confirmatory standard in toxicology and for steroids, drugs, metanephrines.
Resolves many immunoassay interferences (no antibody cross-reactivity).
Labor-intensive and expertise-dependent.
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 5

## Slide 7
CLINICAL CHEMISTRY · IMMUNOASSAY
Immunoassay Design and the Hook Effect
Original schematic. In a sandwich assay, signal tracks analyte — until extreme concentrations saturate the antibodies and the signal paradoxically falls (high-dose hook).
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 6

## Slide 8
CLINICAL CHEMISTRY · IMMUNOASSAY
Two Designs, Opposite Signal Logic
SANDWICH (IMMUNOMETRIC)
Capture antibody + analyte + labeled detection antibody.
Signal is directly proportional to analyte — used for larger molecules (TSH, hCG, troponin).
Vulnerable to the high-dose hook effect at extreme concentrations.
Needs two epitopes, so very small analytes can’t use it.
COMPETITIVE
Analyte competes with labeled antigen for limited antibody.
Signal is INVERSELY proportional to analyte — used for small molecules (cortisol, drugs, T4).
No hook effect in the same way, but cross-reactivity matters.
Calibration curves are nonlinear.
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 7

## Slide 9
CLINICAL CHEMISTRY · IMMUNOASSAY
Immunoassay Interferences You Must Know
ANTIBODY INTERFERENCES
Heterophile antibodies (e.g., HAMA) bridge capture and detection antibodies → false positive/elevation.
Suspect when a result doesn’t fit the clinical picture (e.g., implausibly high hCG, troponin).
Confirm with serial dilution (non-linearity), heterophile blocking tubes, or an alternative platform.
Macro-analytes (macroprolactin, macro-CK) cause spurious elevations.
BIOTIN & HOOK
High-dose biotin (supplements) interferes with streptavidin-biotin assays — can falsely raise or lower results by design.
Classic pattern: low TSH with high free T4 mimicking hyperthyroidism.
The hook effect makes a very high analyte read falsely low — dilute and re-assay if suspected.
Always reconcile a surprising value with the clinical context.
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 8

## Slide 10
02
PART TWO
Sample Interferences & the Testing Cycle

## Slide 11
CLINICAL CHEMISTRY · INTERFERENCES
Hemolysis, Icterus, Lipemia (HIL)
Interferent | Mechanism | Classic effects
Hemolysis | Release of intracellular contents + spectral interference | ↑ potassium, ↑ LDH, ↑ AST, ↑ phosphate; ↑ free hemoglobin
Icterus | High bilirubin alters absorbance | Interferes with several colorimetric assays (assay-dependent direction)
Lipemia | Turbidity scatters light; volume displacement | Spurious results; pseudohyponatremia by indirect ISE
In vitro / preanalytic | Tourniquet, fist-clench, delayed separation | ↑ potassium, ↑ lactate; spurious changes
Automated HIL indices flag affected samples; the corrective action is to recollect or use an interference-resistant method.
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 9

## Slide 12
CLINICAL CHEMISTRY · THE TESTING CYCLE
Error Across the Testing Cycle
PREANALYTIC
order, collect, label, transport, process
ANALYTIC
measurement on the instrument
POSTANALYTIC
result, interpretation, reporting
Most errors are PREANALYTIC: wrong patient/tube, hemolysis, clotting, wrong additive, delayed processing.
Analytic errors: calibration drift, interference, carryover — caught by quality control and delta checks.
Postanalytic errors: transcription, wrong reference interval, failure to communicate a critical value.
Delta checks compare a new result with the patient’s prior value to catch sample mix-ups and large shifts.
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 10

## Slide 13
CLINICAL CHEMISTRY · QUALITY CONTROL
Detecting Analytic Error
QC FUNDAMENTALS
Run controls at defined intervals; plot on a Levey-Jennings chart against mean ± SD.
Random error widens scatter (precision); systematic error shifts/trends the mean (accuracy).
Westgard multirules (e.g., 1₃ₛ, 2₂ₛ, R₄ₛ, 10ₓ) flag out-of-control runs.
A shift suggests a new lot/calibration; a trend suggests reagent or electrode deterioration.
BEYOND QC
Proficiency testing benchmarks performance against peers.
Delta checks and absurd-value limits catch sample and analytic problems.
Calibration verification and linearity confirm the reportable range.
Method comparison and bias assessment when changing platforms.
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 11

## Slide 14
03
PART THREE
Cases & Board Review

## Slide 15
CLINICAL CHEMISTRY · CASE 1
Case 1
CLINICAL VIGNETTE
A potassium of 7.2 mmol/L is reported on a well outpatient with a normal ECG. The sample is noted to be visibly hemolyzed, and the LDH and phosphate are also elevated. A repeat, carefully drawn sample is normal.
?
What explains the first result, and what is the lesson for reporting?
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 12

## Slide 16
CLINICAL CHEMISTRY · CASE 1 · RESOLUTION
Case 1: Hemolysis-Induced Pseudohyperkalemia
In vitro hemolysis released intracellular potassium (and LDH, AST, phosphate) → spurious hyperkalemia.
The clinical mismatch (well patient, normal ECG) is the tell.
The HIL index and the recollected normal result confirm the artifact.
Report with a hemolysis comment or recollect — never let a spurious critical potassium drive treatment.
TEACHING POINT
Hemolysis is the commonest interference; potassium, LDH, AST, and phosphate move up together. Always reconcile criticals with the patient.
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 13

## Slide 17
CLINICAL CHEMISTRY · CASE 2
Case 2
CLINICAL VIGNETTE
A non-pregnant patient has a markedly elevated hCG, but imaging shows no pregnancy or tumor. Serial dilution of the sample does not yield proportional results, and a different platform reports a normal value.
?
What interference is most likely, and how did the laboratory confirm it?
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 14

## Slide 18
CLINICAL CHEMISTRY · CASE 2 · RESOLUTION
Case 2: Heterophile-Antibody Interference
Heterophile antibodies bridged the assay antibodies, producing a false-positive hCG.
Non-linearity on dilution is a classic clue to interference.
Confirmation: a normal result on an alternative platform (and/or heterophile-blocking tubes).
Recognizing this prevents harmful work-ups or therapy for a non-existent condition.
TEACHING POINT
When an immunoassay result defies the clinical picture, think interference: dilute, block, or switch platforms before acting.
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 15

## Slide 19
CLINICAL CHEMISTRY · CASE 3
Case 3
CLINICAL VIGNETTE
A patient on high-dose biotin supplements has a suppressed TSH with a high free T4, suggesting hyperthyroidism, but is clinically euthyroid. Repeat testing after stopping biotin is normal.
?
What caused the pattern, and what advice prevents it?
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 16

## Slide 20
CLINICAL CHEMISTRY · CASE 3 · RESOLUTION
Case 3: Biotin Interference
High-dose biotin interferes with streptavidin-biotin immunoassays, mimicking hyperthyroidism (low TSH, high free T4).
The direction depends on assay design (sandwich vs competitive).
Advise holding biotin (often ~48–72 h) before testing.
Reconcile thyroid results with the clinical state before acting.
TEACHING POINT
Ask about biotin supplements when thyroid (or troponin) results don’t fit — a simple history prevents a misdiagnosis.
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 17

## Slide 21
04
PART FOUR
Board Review

## Slide 22
CLINICAL CHEMISTRY · BOARD REVIEW · Q1
Board-Style Review
A sandwich immunoassay reports an unexpectedly LOW value in a patient you suspect has a very high analyte level. What is the best next step?
A. Report the low value
B. Dilute the sample and re-assay (suspect hook effect)
C. Add more conjugate
D. Switch to a competitive assay only
E. Repeat without changes
ANSWER B — Dilute and re-assay (hook effect)
Extremely high analyte saturates a sandwich assay’s antibodies and lowers the signal (high-dose hook). Dilution relieves saturation and yields the true, higher value.
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 18

## Slide 23
CLINICAL CHEMISTRY · BOARD REVIEW · Q2
Board-Style Review
Which set of analytes characteristically rises together due to in vitro hemolysis?
A. Sodium, chloride, glucose
B. Potassium, LDH, AST, phosphate
C. Calcium, albumin, ALP
D. Bicarbonate, BUN, creatinine
E. TSH, free T4
ANSWER B — Potassium, LDH, AST, phosphate
These are concentrated intracellularly; red-cell lysis releases them, producing concordant spurious elevations and signaling hemolysis.
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 19

## Slide 24
CLINICAL CHEMISTRY · BOARD REVIEW · Q3
Board-Style Review
On a Levey-Jennings chart, the control mean gradually drifts upward over two weeks. This pattern indicates:
A. Random error
B. A trend, suggesting systematic error (e.g., reagent/electrode deterioration)
C. Normal variation
D. A shift from a new lot
E. Clerical error
ANSWER B — A trend (systematic error)
A gradual, progressive drift is a trend, indicating systematic error such as deteriorating reagent or a failing electrode. An abrupt step is a shift (e.g., new lot/calibration).
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 20

## Slide 25
CLINICAL CHEMISTRY
Key Take-Home Points
1
Know what each method measures: spectrophotometry (Beer-Lambert), immunoassay (sandwich vs competitive), and MS (confirmatory).
2
Sandwich assays read high analyte falsely LOW (hook); heterophile and biotin interferences mimic disease — reconcile with the clinic.
3
Hemolysis raises potassium, LDH, AST, and phosphate together; lipemia causes pseudohyponatremia by indirect ISE.
4
Most errors are preanalytic; delta checks and HIL indices catch many before they reach the chart.
5
QC: Levey-Jennings + Westgard rules separate random (precision) from systematic (accuracy) error.
Makassed General Hospital · Department of Laboratory Medicine
21

## Slide 26
CLINICAL CHEMISTRY · REFERENCES & FURTHER READING
References
1. Rifai N, Horvath AR, Wittwer CT (eds). Tietz Textbook of Clinical Chemistry and Molecular Diagnostics, 6th ed. Elsevier, 2018.
2. CLSI EP07: Interference Testing in Clinical Chemistry.
3. CLSI C24: Statistical Quality Control for Quantitative Measurement Procedures.
4. Westgard JO. Basic QC Practices, 4th ed. Westgard QC, 2016.
Makassed General Hospital · Department of Laboratory Medicine
CP Lecture Series · 22